## Slide 1: Konference k transformaci energetiky Energetika 4.0 a tarifní reforma
Ekonomické aspekty rozvoje decentrální energetiky:
Network Tariffs and Economic Incentives
Lubomír Lízal, PhD. Praha, 15. března, 2018

## Slide 2: Real economic convergence of the Czech Republic
kWh/capita
Additional source: IEA, www.iea.org
consumption/dom.supply/production
[TWh]
2005 55 / 70 / 83
2015 54 / 71 / 84
CZ economic convergence
[%EU Avg, in PPP]
2005 74
2015 80

## Slide 3: WEC Energy Outlook

## Slide 4
WEC Electric Energy World Outlook
Three scenarios called Modern Jazz, Unfinished Symphony, and Hard Rock
Electricity Production (TWh) - Total
TPES (MToe) - Total
Different patterns of Electricity
  Continuously rising production (and needs)

## Slide 5: Testing the predictions
    Electric power consumption (kWh per capita)
Time
Source: WB, data.worldbank.org
Electric Energy kWh/capita

## Slide 6: Quick-check results
After 10 years
  Despite the long economic downturn
  Despite massive political pressures (standards, limits, fees etc.) in favor of energy savings
  Despite the subsidies on energy savings
  The absolute electric energy consumption has not decreased but rather stagnated
    Limited relative convergence of CZ is a question for future
      Stagnation vs. increase of consumption
      Decrease unlikely

## Slide 7: Quick-check of conditions
After 10 years
  Energiewende
    Closure of nuclear power plants in Germany
    Faster phase-out/closures of coal plants
  Yet no new economically viable technologies of storage
  Cheaper technologies for unstable generations
    Photovoltaic, wind
  Almost all new investments are based on
    Subvention schemes
  Crowding out any private investment
      Economic reasons
      Political uncertainty (e.g., BAT, tariffs, other legal changes )
  Only distorted market/price signals

## Slide 8: Starting Points
Current grid tariff structures either based on
  volume consumed
  or on the capacity (exceptionally)
Future needs of final customers, (decentralized) generators, distribution system operators (DSOs) have to be reflected.
European policy on energy efficiency (Energy Efficiency Directive) should (ideally) lead to
  lower consumption
  lower volumes of electricity (gas etc.) transported on the grid

## Slide 9: Consequence of Low Volumes
However that implies no direct cost‐reducing effect for network operators:
Costs
  are predominantly INDEPENDENT on volume
  determined by (past and future) investments in network capacity (i.e., fixed costs)
  based on current and expected connection capacity
However, structure of grid tariffs determines behavior of players (assuming they cover networks costs) and can help or worsen the transformation process

## Slide 10: Higher distribution costs
The opposite regarding future costs is true:
  an increasing amount of distributed generation will require higher investments DSOs networks
  New components and IT grid monitoring, automation and procurement of flexibility services will lead to higher distribution costs per unit.
The in‐feed of renewable energies (sun or wind) are not controllable (only shut-downs) and to overcome the challenge we need for more flexibility
  on the demand side
  on the supply side
  for services that can facilitate the flexible arrangements

## Slide 11: Policy objectives
Policy objectives of distribution and security
Tariffs should:
  ensure well‐functioning of the electricity markets
  encourage energy efficiency
  encourage the development of distributed generation
  contribute to system flexibility through supply/demand response
    Long-term (correct signals whether to build new generating resources or adopt new technologies on the demand side)
    Short-term (adjust required demand/supply patterns)
    Immediate (shift demand, provide active stability support)

## Slide 12: Economic Principles of Grid Tariffs
General and specific economic principles should be met:
Cost reflectiveness
  should reflect the costs incurred by serving each user
Infrastructure cost efficiency
  reduce infrastructure costs by reducing/shifting peak demand
Operational cost efficiency
  low operational, administrative and monitoring costs
Revenue adequacy
  ensure full recovery of network cost and return on capital
Transparency
  transparent, auditable, and (time) consistent

## Slide 13: Conflicting Priorities
Combining together: Conflicts
 | Volume | Capacity
 | [CZK/kWh] | [CZK/kW, CZK/kVA]
Economic Principles of Grid Tariffs |  | 
Cost reflectiveness | -- | ++
Infrastructure cost efficiency | -- | ++
Operational cost efficiency | -- | ++
Revenue adequacy | -- | ++
Transparency | - | ++
Policy Objectives |  | 
Market functioning | - | -
Distributed generation | ++ | --
System flexibility | ++ | --
Energy efficiency | ++ | --

## Slide 14: No Easy Way Out
Multiple component tariffs for distribution (DSOs):
fixed tariff per customer
  covers fixed costs (e.g., metering, mailing, billing)
capacity tariff
  covers capacity related costs
volume tariff
  covers volume related costs

## Slide 15: Tariffs and Complexity
Shifting consumption to off peak period
  higher tariffs at peak times
Varying grid tariffs deliver economic incentives for the efficient use of the network
Complex time tariffs require SMART (time-dependent) metering
Tariffs can allow an adequate response but:
  High number of time periods lead to complexity and less transparency
  Real time (dynamic) complex grid tariffs require automation operated by service providers and is opaque
  Regular end-customers can not deal with complexity
    HI-LO is enough

## Slide 16: Hybrid Tariffs
Combining volume and capacity elements
  Flat component
    fixed payment per customer
  Power component
    per kW (measured capacity) or per kVA (connection capacity)
  Energy component
    per kWh
      Proportionate
      Progressive
      Degressive
      Differential

## Slide 17: Hybrid Tariffs: Progressive Capacity Element
Hybrid tariffs with progressive capacity element
Advantages:
  Facilitates the transition from volume to capacity
  Reduces the financial impact of the transition for the final customer
  Better orientation of customer choice to the most suitable connection capacity level
  Can function without SMART meters in connection capacity
Requirements:
  connection capacity of every individual customers is known
    This is not equivalent to the distribution circuit-breaker
  for the measured capacity smart meters needed anyway

## Slide 18: Dynamic pricing
Adverse effects of dynamic retail pricing
Price signals should promote active change of consumer behavior in return for financial benefits
  price signals: time-differentiated pricing systems, time-of-use pricing (e.g. peak and off-peak prices) or real-time pricing
Low energy prices due to abundant supply
  => create a peak on the network due excessive increase in consumers’ consumption simultaneously
  => consequently the network tariff should be high
Dynamic network tariffs can create unstable behavior
  Proper weighting necessary

## Slide 19: SMART Grids
Neutral market – the DSO – and the tariff structure
all flexibility resources (e.g. generation, storage and demand) compete on a level playing field
Needed:
improvement of infrastructure (strengthening the grids);
addition of the digital layer
business process models to allow the economic benefits of the SMART elements materialize

## Slide 20: SMART Grids
Key features of the smart grid:
IT / data communication
  Cyber-security
SMART meters
  an essential part
  increased data granularity with time-based metering used either by the DSO or by the market parties.
Control and monitoring of the grid enabling:
  Flexibility in network topology (photo-voltaic (PV) installation, EVs, Flexible storage facilities, etc.)
  Load adjustment / Load balancing
  Peak curtailment
  Improved reliability

## Slide 21: Cars and public budgets
Electric vehicles are often exempt from taxes and other regulations (e.g., parking…)
Creates distorted incentives with potential problem in the future (e.g., excessive PV compesation case in CZ)
  Excise tax proceeds in CZ ~ 80mld. CZK (plus 16ml. VAT)
  Total about ~100mld CZK
  The more EV the higher pressure to on tax proceeds
  Tax on EV will be levied => structural change inevitable

## Slide 22: DSO Tariffs
Network tariff structures should really reflect the cost incurred by the behavior of the connected customer.
  The one who is inducing extra costs should pay more
    and more than the one who does not induce these
Proper incentives
  increases the value of flexibility
  stimulate the development of devices and services
A well-designed tariff is the accelerator of the development of flexibility.

## Slide 23: Incentives and DSO Tariffs
Multiple elements:
Tariff basis
  Capacity: reflects better the cost for the network
  Consumption: stimulation to energy saving measures.
Timing
  Fixed timing (e.g. discount at off-peak hours)
  Dynamic (real-time depending on the current state of the local/global network)
Direction
  Consumption
  Production
Location
  tariff structure per DSO area
  locational tariff

## Slide 24: Combined DSO Tariffs
Combined tariff structure
  the simpler a tariff structure is, the easier it is to understand
  the more effective usually is
Network tariff based on consumption no longer correctly reflects the network costs
  The real costs depends on required peak capacity.
Example 1 (good)
  symmetrical capacity bandwidth
  exceeds of the bandwidth automatically charged with an extra fee. Incentive to stay as much as possible within the bandwidth
    e.g. to charge an EV smoothly during night hours

## Slide 25: Net metering
A well-designed tariff structure stimulates the development of flexibility instead of blocking it.
Example 2 (bad)
    net metering
      Right use that electricity at any time
      No control when electricity is generated
      applied daily/monthly/quarterly/annually
  The longer the period the lesser it stimulates own management
Net metering puts the burden of stabilizing the production and consumption at DSO and other market parties
Does not stimulate the further development of flexibility.

## Slide 26: Thank you for your attention
www.ciirc.cvut.cz
www.fel.cvut.cz
Lubomír Lízal, PhD.
lubomir.lizal@cvut.cz